LINUX NETWORK COMMANDS

1. ifconfig Command

Interface configurator - display your ip address, network interfaces, transferred and received data information, configure a network interface. On most modern distributions ifconfig has been depracated, use ip instead.

Syntax
      ifconfig [interface]
where interface is the name of the interface.
        Usually a driver name followed by a unit number, eth0 = 1st Ethernet interface.
If no arguments are given, ifconfig displays the status of the currently active interfaces. If a single interface argument is given, it displays the status of the given interface only; if a single -a argument is given, it displays the status of all interfaces, even those that are down. Otherwise, it configures an interface.
eth0 is the first ethernet interface. (Additional ethernet interfaces would be named eth1, eth2, etc.) This type of interface is usually a NIC connected to the network by a category 5 cable.

lo is the loopback interface. This is a special network interface that the system uses to communicate with itself.

wlan0 is the name of the first wireless network interface on the system. Additional wireless interfaces would be named wlan1, wlan2, etc.
### Media access control functions
ifconfig is also commonly used to change the media access control (MAC) address of an interface. In this process, the network interface is first disabled (set down) with the ifconfig command, followed by a MAC change command:
ifconfig wlan0 down
ifconfig wlan0 hw ether 00:11:22:33:44:55
ifconfig wlan0 up
#### Enable or Disable Specific Interface
To enable or disable specific Interface, we use example command as follows.
##### i) To Enable eth0:
 ifup eth0
ii)To Disable eth0

ifdown eth0
iii)To Setting MTU Size
ifconfig eth0 mtu XXXX
By default MTU size is 1500. We can set required MTU size with below command. Replace XXXX with size.
iv) To Set Interface in Promiscuous mode
 ifconfig eth0 – promisc
Network interface only received packets belongs to that particular NIC. If you put interface in promiscuous mode it will received all the packets. This is very useful to capture packets and analyze later. For this you may require superuser access.

2. PING Command
PING (Packet INternet Groper) command is the best way to test connectivity between two nodes. Whether it is Local Area Network (LAN) or Wide Area Network (WAN). Ping use ICMP (Internet Control Message Protocol) to communicate to other devices.
Syntax
ping ip or host name
ping 8.8.8.8
ping www.google.com
n Linux ping command keep executing until you interrupt. Ping with -c option exit after N number of request (success or error respond).
ping -c 5 www.google.com

3. TRACEROUTE Command
traceroute is a network troubleshooting utility which shows number of hops taken to reach destination also determine packets traveling path. Below we are tracing route to global DNS server IP Address and able to reach destination also shows path of that packet is traveling.
Syntax
traceroute ip
traceroute 4.2.2.2
4. NETSTAT Command
Netstat (Network Statistic) command display connection info, routing table information etc. To displays routing table information use option as -r.
Syntax
netstat -r
netstat (network statistics) is a command line tool for monitoring network connections both incoming and outgoing as well as viewing routing tables, interface statistics etc. netstat is available on all Unix-like Operating Systems and also available on Windows OS as well. It is very useful in terms of network troubleshooting and performance measurement. netstat is one of the most basic network service debugging tools, telling you what ports are open and whether any programs are listening on ports.
Listing all the LISTENING Ports of TCP and UDP connections
Listing all ports (both TCP and UDP) using netstat -a option.
netstat -a | more
Listing TCP Ports connections
Listing only TCP (Transmission Control Protocol) port connections using netstat -at.
Listing UDP Ports connections
Listing all active listening UDP ports by using option netstat -lu.
5. NSLOOKUP Command
nslookup command also use to find out DNS related query.
nslookup www.tecmint.com
Server: 4.2.2.2
Address: 4.2.2.2#53
Non-authoritative answer:
www.tecmint.com canonical name = tecmint.com.
Name: tecmint.com
Address: 50.116.66.136
#### Find out “A” record (IP address) of Domain
nslookup yahoo.com
Server: 4.2.2.2
Address: 4.2.2.2#53
Non-authoritative answer:
Name: yahoo.com
Address: 72.30.38.140
Name: yahoo.com
Address: 98.139.183.24
Name: yahoo.com
Address: 209.191.122.70
Above command query domain www.yahoo.com with 4.2.2.2 public DNS server and below section shows Non-authoritative answer: displays A record of www.yahoo.com
#### Find out Reverse Domain Lookup
nslookup 209.191.122.70
Server: 4.2.2.2
Address: 4.2.2.2#53
Non-authoritative answer:
70.122.191.209.in-addr.arpa name = ir1.fp.vip.mud.yahoo.com.
Authoritative answers can be found from:
6.ROUTE Command
route command also shows and manipulate ip routing table.
 route
Kernel IP routing table
Destination Gateway Genmask Flags Metric Ref Use Iface
192.168.50.0 * 255.255.255.0 U 0 0 0 eth0
link-local * 255.255.0.0 U 1002 0 0 eth0
default 192.168.50.1 0.0.0.0 UG 0 0 0 eth0
Adding, deleting routes and default Gateway with following commands.
##### Route Adding
route add -net 10.10.10.0/24 gw 192.168.0.1

##### Route Deleting
route del -net 10.10.10.0/24 gw 192.168.0.1
##### Adding default Gateway
route add default gw 192.168.0.1
### 7. HOST Command
host command to find name to IP or IP to name in IPv4 or IPv6 and also query DNS records.
# host www.google.com
www.google.com has address 173.194.38.180
www.google.com has address 173.194.38.176
www.google.com has address 173.194.38.177
www.google.com has address 173.194.38.178
www.google.com has address 173.194.38.179
www.google.com has IPv6 address 2404:6800:4003:802::1014
Using -t option we can find out DNS Resource Records like CNAME, NS, MX, SOA etc.
# host -t CNAME www.redhat.com
www.redhat.com is an alias for wildcard.redhat.com.edgekey.net.
### 8. ARP Command
ARP (Address Resolution Protocol) is useful to view / add the contents of the kernel’s ARP tables. To see default table use the command as.
# arp -e
Address HWtype HWaddress Flags Mask Iface
192.168.50.1 ether 00:50:56:c0:00:08 C eth0
9. HOSTNAME Command
hostname is to identify in a network. Execute hostname command to see the hostname of your box. You can set hostname permanently in /etc/sysconfig/network. Need to reboot box once set a proper hostname.
# hostname
tecmint.com